## Slide 1: Bobcat Enrichment Facility
???
Maryland Zoo

## Slide 2: Overview
Can also be adapted to other animals (such as elephants).
For now, adjusting audio volume and type is not working.

## Slide 3: Build your own facility
Step-by-step

## Slide 4: Network & Connections
Coordinator
Detector #1
Feeder #n+1
Detector #n
…
Feeder #n+m
…
Wireless
Build your own enrichment facility.
Add as many detector and feeder devices as you need.

## Slide 5: Hardware
Coordinator
LCD × 1
Rotary Encoder × 1
Keypad × 1
XBee × 1
Detector
Arduino nano × 1
Distance sensor × 1
Speaker× 1
MP3 player × 1
XBee × 1
Arduino nano × 1
Need a photo here
Need a photo here
SD card × 1
Relay × 1
Resistor 100 Ω × 1
Voltage regulator × 1
Battery × 1
Voltage regulator × 1
Battery × 1

## Slide 6: Hardware
Feeder
Relay × 1
XBee × 1
Arduino nano × 1
Actuator × 1
Voltage regulator × 1
Battery × 1
(Auger version)
(Linear actuator version)
or

## Slide 7: Purchase log
Name | Link | Note
Arduino nano | Link | 
XBee | Link | Should all have the same series (e.g., S2C). Should try other series for long-distance communication.
XBee adapter | Link | Better to have both USB and Serial ports
Voltage regulator | Link | 
Battery | Link | 
DC power cable | Link | 
Liquid crystal displayer | Link | Should be 20 × 4, should have I2C adapter (a small circuit at the back)
Rotary encoder | Link | 
Keypad | Link | Should be 4 × 4
Distance sensor | Link | Should try RCWL-1670 as a cheap replacement
Speaker | Link | 
DFPlayer MP3 MP3-TF-16P | Link | 
SD card | Link | 
Relay (1 channel) | Link | Identify whether the relay is high or low level trigger. Adjust code accordingly.
Relay (2 channel) | Link | 
Resistor 100 Ω | Link | 

## Slide 8: Hardware Preparation – Voltage Regulator
Do these for all voltage regulators before assembling the hardware.
Tune the resistor (yellow arrow) so that the output voltage is 5 volts.

## Slide 9: Hardware Preparation – XBee
Do these for all XBee modules before assembling the hardware.
Assemble the XBee chip (irregular shape) to the adaptor (regular shape)
Connect USB port to a PC
Follow this tutorial to initialize XBee: https://www.instructables.com/How-to-Use-XBee-Modules-As-Transmitter-Receiver-Ar/
  Make sure that all the XBees share the same Channel but have different PAN ID.

## Slide 10: Hardware Preparation – Identifying Trigger Types
Do these for all relays:
Identify whether the relay is a high- or low-level trigger.
If it is adjustable, put the jumper on the low-level trigger.
If it is not adjustable, most relays are low-level triggers by default.
If it is a high-level trigger, revise the code accordingly (see later).

## Slide 11: Hardware Preparation – Modifying Keypad
Paste stickers on the Keypad to change the keys.
OK
↑
↓
→
←

## Slide 12: Hardware Preparation – SD card
Do these for all SD cards.
Add audio files.
Naming request for these files?

## Slide 13: Wiring for Coordinator

## Slide 14: Wiring for Detector
Color code is important here

## Slide 15: Wiring for Feeder (Auger Version)

## Slide 16: Wiring for Feeder (Linear Actuator Version)

## Slide 17: Software – Arduino
Download Arduino IDE 2.x.x installer: https://www.arduino.cc/en/software
Install Arduino IDE 2. Just use the default settings.
Open Arduino IDE. Whatever it asks your permission to install, allow them.
Install these libraries (and ):
  Liquide Crystal I2C by Frrank de Brabander
  Button by Michael Adams
  Keypad by Mark Stanley et al
  RotaryEncoder by Matthias Hertel
  DFRobotDFPlayerMini by DFRobot
  arduino-timer by Michael Contreras

## Slide 18: Software – Fixing Bugs in Library
For a library, DFRobotDFPlayerMini's current version (1.0.6) has some small bugs.
They may fix it in further versions.
Add "_isSending = 0;" at the end of line 37 in DFRobotDFPlayerMini.cpp.

## Slide 19: Software – Uploading Codes on Arduinos
Do these for all Arduinos:
Connect Arduino with the PC using USB.
Open the code using IDE
  Coordinator: coordinator_nano.ino
  Detector: detector_nano.ino
  Feeder: feeder_nano.ino
Modify the code
  Only modify the first few lines. Before “#include”.
  Each detector and feeder should have a separate ID number, which should be a positive integer. For example, detector #1 and feeder #1 cannot be in the system together. Detector #0 is not OK.
Select board as nano
Upload code

## Slide 20: Hardware – Adjusting LCD Backlight

## Slide 21: Technical Documentation
For further development
Usually, you don’t need to know this

## Slide 22: Communication Protocol
The messages are in fixed lengths to ensure reliable communication.
To simplify the network, each feeder node only communicates with the base nodes.
From coordinator to nodes: “<[node_ID, 3][cmd, 3][planned_timeout_sec, 4][planned_distance, 4]>”.
  The numbers are digit numbers.
  Node_ID: showing which node (detector or feeder) the coordinator wants to communicate to.
  Cmd: command. 100: Detector tries to detect animal. 101: Feeder feeds once. Others: Doing nothing.
  Planned_timeout_sec: the time span (unit: second) that the detector keeps monitoring before replying that the animal fails to move close. It is only useful for detectors.
  Planned_distance: the distance (unit: mm) the animal is determined to have moved close. Only useful for detectors.
  For example, <0011000300100> means the coordinator asks detector #1 to monitor if the animal moves closer than 100 mm in 30 seconds.
From nodes to coordinator: “<[coordinator_ID = 000, 3][node_ID, 3][is_success, 1]>”.
  The numbers are digit numbers.
  Coordinator_ID: Shows that the node wants to communicate with the base. It is always 000.
  Node_ID: Showing which node initiated this communication.
  Is_success: Showing whether the animal has moved close in time (detector) or the food ball has been released (feeder).
  For example, <0000010> means that detector #1 has not identified that the animal moves close to the time threshold.

## Slide 23: Range of Distance Detector